## Slide 1: OEL : ต้องเข้าใจจึงจะประเมินได้ถูกต้อง
Choochot Sutthiboriban,CIH
October 22,2019

## Slide 2: outlines
What is OEL
How to set OEL
How we apply OEL in IH and OH
OEL Decision logic

## Slide 3
HYGIENE STANDARDS AND OCCUPATIONAL EXPOSURE LIMITS
What is OEL??

## Slide 4
Hygiene Standards
Hygiene standard:
The level of exposure, via inhalation, that should not cause ill health to a healthy adult when exposed to the contaminant
Other (interchangeable) terms include:
Threshold limit values
Exposure standards
Occupational exposure limits
Workplace exposure limits

## Slide 5: Hygiene Standards or Occupational Exposure Limits (OELs)
They are not an index of toxicity
They do not represent a fine demarcation between good and bad practice.
They are based on the current best available information and are liable to change.
If there is not a hygiene standard set for a chemical substance, it does not mean that substance is safe.
Good occupational hygiene practice is to keep airborne contaminants to as low a level as possible, not to just below the relevant hygiene standard(s).
They apply to occupational exposure of adults. They are not applicable to environmental exposure where more susceptible groups exist e.g. pregnant women, children, infirm.
For chemicals they generally relate to airborne concentrations i.e. they only take into account the inhalation route of entry.
They generally refer to single substances, although some guidance may be given on mixed exposures.

## Slide 6: Occupational exposure limit (OEL)
Occupational exposure limit is an upper limit on the acceptable concentration of a hazardous substance in workplace air for a particular material or class of materials. It is typically set by competent national authorities and enforced by legislation to protect occupational safety and health. It is an important tool in risk assessment and in the management of activities involving handling of dangerous substances . (Wigipedia)
Threshold Limit Value – Time-Weighted Average (TLV-TWA): The concentration of a hazardous substance in the air averaged over an 8-hour workday and a 40-hour workweek to which it is believed that workers may be repeatedly exposed, day after day, for a working lifetime without adverse effects.

## Slide 7
OELs are set to protect workers
  8/hr/day, +
  5 days/week, +
  52 weeks/year …..
  for 40 years of working lifetime
Therefore:
Repeated exposure studies are REQUIRED!
  Assess safe CHRONIC (low levels) exposure level based on NOELs and NOAELs, for various endpoints that might contribute to the health of a worker with
    Chronic: Long-term/low level exposures (e.g. mutagenicity, genotoxicity, carcinogenicity, blood, or other target organ effects
    Sub-chronic: >90 days exposure that result in health effects (e.g. mutagenicity, reproductive/developmental effects
Occupational exposure limit (OEL)

## Slide 8
Tasks vs. Full Shift
Most OELs are set for 8-hour TWA
Where irritation or severe acute toxicity occurs:
  Short Term Exposure Limit (STEL with time specified)
  “Excursion” – allowable concentrations for short periods of time (e.g. “task”)
  Ceiling or Peak (never exceed)

## Slide 9
Why Do We Have OELs?
Worker protection at “safe” exposure levels
There is little point in “monitoring” if you don’t know a ‘safe’ level

## Slide 10
How to set OEL?

## Slide 11: Setting of Hygiene Standards and Exposure Limits
There are three main types of hygiene standards:-
  Chemical agents such as gases, vapours, fumes, mists, dusts and aerosols.
  Physical agents such as noise, vibration, heat, cold and radiation (ionising and non‑ionising)
  Biological exposure indices.

## Slide 12: Setting of Hygiene Standards and Exposure Limits
When setting hygiene standards for hazardous agents, the effects the agents might have on the body have to be considered namely:-
  Contact
  Local toxic effects at the site of contact (skin, eye, respiratory tract etc.)
  Absorption
  Transport, Metabolism, Storage
  Systemic toxic effects, remote from the site of contact (any organ system e.g. blood, bone, nervous system, kidney etc.)
  Excretion
  Acute toxicity i.e. the adverse effects occur within a short time of exposure to a single dose, or to multiple doses over 24 hours or less e.g. irritation, asphyxiation, narcosis
  Chronic toxicity.

## Slide 13: Setting of Hygiene Standards and Exposure Limits
The data for setting hygiene standards includes the use of:
  Animal studies
  Human research and experience
  Epidemiology (the statistical study of disease patterns in groups of individuals)
  Analogy.

## Slide 14
Hygiene Standards (OEL) for Chemical Agents
Limit | Country / Union
TLV – Threshold Limit Value | USA
MAK - Maximale Arbeitsplatz-Konzentration | Germany
MAC | Russia
WEL – Workplace Exposure Limit | United Kingdom
IOELVs (Indicative Occupational Exposure Limit Value) | Europe
OES – Occupational Exposure Standards | Australia
WES – Workplace Exposure Standards | New Zealand
ประกาศกรมสวัสดิการและคุ้มครองแรงงาน - เรื่อง ขีดจํากัดความเข้มข้นของสารเคมีอันตราย (2560) | Thailand
Only a few countries have organisations with the appropriate resources for setting limits. Most countries base limits on the following:

## Slide 15: Quantifying Airborne Concentrations of Chemical Agents
Airborne contaminants can be quantified in several ways;
By volume - atmospheric concentration in parts per million (ppm)
(Gas & Vapor)
By weight - milligrams of substance per cubic metre of air (mg.m-3).
(Aerosol & Particulates)

## Slide 16: Categories of Exposure Limits
Long Term Exposure Limits are expressed as a Time Weighted Average (TWA) normally over an eight hour period. This allows for exposures to vary through the working day so long as the average exposure does not exceed the limit.
Short Term Exposure Limit (STEL) normally over a 15 minute period are used when exposure for short periods of time occurs.
Ceiling Limits are sometimes used and are concentrations that should not be exceeded during any part of the working exposure.
"Skin" Notation - Substances can have a contributing exposure effect by the cutaneous route (including mucous membranes and eyes).

## Slide 17: Effects of Mixed Exposures
Synergistic substances: known cases of synergism are considerably less common than the other types of behaviour in mixed exposures.
Additive substances: where there is reason to believe that the effects of the constituents are additive, and where the WELS are based on the same health effects, the mixed exposure should be assessed using a formula.
Independent substances: where no synergistic or additive effects are known or considered likely, the constituents can be regarded as acting independently and the measures needed to achieve adequate control assessed for each separately.

## Slide 18: Calculation of exposure with regard to the specified reference periods
TWA : The 8-hour reference period
Exposures treated as equivalent to a single uniform exposure for 8 hours (the 8-hour time-weighted average (TWA) exposure).
Represented mathematically by:
C1 x T1 + C2 x T2 + ……. Cn x Tn
8
Where:
C1 is the occupational exposure
T1 is the associated exposure time in hours in any 24-hour period.
The short-term reference period (STEL): Exposure should be recorded as the average over the specified short-term reference period (usually 15 minutes) and should normally be determined by sampling over that period.

## Slide 19: Biological Monitoring Guidance Values
Complimentary technique to air monitoring.
Biological monitoring is the measurement and assessment of hazardous substances or their metabolites in tissues, excreta or expired air in exposed workers.
Measurements reflect absorption of a substance by all routes.
Particularly useful where exposure is by routes other than inhalation
In most cases limits for Biological Monitoring are not statutory.
Biological monitoring undertaken needs to be conducted on a voluntary basis (i.e. with the fully informed consent of all concerned).

## Slide 20: Calculation of Additive Effects

## Slide 21: When Should I Calculate Additive Effects of the Involved Chemicals?
If exposures are to multiple chemicals that have the same target organ, an exposure acceptability test may be appropriate
  Use the calculation on next slide …
Calculation of Additive Effects
Notes: If exposures are to multiple chemicals that have the same target organ, an exposure acceptability test may be appropriate. Use the test for "Mixtures with Additive Effects" in the ACGIH TLV book.
Consult with your industrial hygienist if you think that additive effects may be an issue.

## Slide 22: Calculation of Additive Effects
The test for "Mixtures with Additive Effects" is in line with the ACGIH TLV book:
For acceptable exposure results
C1 + C2 + C3 + …. = must be less than 1
T1 T2 T3
Where C1 = Concentration of component 1 …
And T1 = OEL of component 1 …
Notes: The test for "Mixtures with Additive Effects" in the ACGIH TLV book: For acceptable exposure,
C1 + C2 + C3 + …. < 1
T1 T2 T3
Where C1 = Concentration of component 1 …
And T1 = OEL of component 1 …

## Slide 23
OEL Notations
  Skin (“S”)
  Respirable and Total Fractions
  Sensitization (Dermal & Respiratory)
    SEN
    R-SEN
    D-SEN
  Carcinogenicity
These are part of the OEL !!!

## Slide 24
Limitations of Hygiene Standards (OEL)
Values do not exist for all substances
Apply to the workforce – workers healthier than general public
Not meant to apply to general population
  Not for environment or boundary emission standards
  Not for use with a set safety factor e.g. divide by 100
Not a fine line between safe and dangerous concentrations
For use by trained occupational hygienists

## Slide 25
How we apply OEL in IH and OH?

## Slide 26: Key elements of an IH Program
  Anticipate or predict potential problems
  Recognize Identify potential hazards
  potential worker hazards in the workplace
  Evaluate the risks of illness or injury resulting from exposure to workplace hazards :
  Qualitative or Quantitative assessment
  Design & Implement “Control Strategies” to mitigate risk of exposure to those hazards
Control
Recognize
Evaluate
Anticipate
Notes: Industrial Hygiene is often defined as the science of anticipating, recognizing, evaluating, controlling, and confirming mitigation of workplace conditions that may cause workers' injury or illness.

## Slide 27: Risk = Hazard x Exposure
Hazard = Hungry Tiger
Exposure = Close to Tiger
Risk of getting eaten is HIGH
Hazard = Hungry Tiger
Exposure = Close to “Caged” Tiger
Risk of getting eaten is LOW
Highly Toxic Chemical
No PPE on bench top
PPE on a bench top
PPE in a fume hood
Hazard Exposure Risk
High
Moderate
Low

## Slide 28: Risk and Hazard ?
Shark is the hazard in the sea
You have never swum (in the sea).
Is there any risk from the Shark?

## Slide 29: How we utilize OEL
Tasks
Employees
Job Groups
Hazard Identification
Anticipation & Recognition
(Chemical, Physical, Biological, Ergonomic)
Risk Assessment
(Qualitative Exposure Assessment)
Priority Rating
IH Monitoring
Follow Up
(Exposure Controls)
IH Stat > OEL ?
OEL
OEL
Yes
No

## Slide 30: How we utilize OEL in IH & OH
Exposure Assessment and Control
& Exposure Monitoring (QEA)
Hazard Awareness,
Personal Protective Equipment
Respiratory Protection
Hearing Conservation
Fume Hood
Ventilation
Indoor Air Quality
Workplace Hygiene
Thermal Stress Prevention
Radiation
OEL & 50%OEL Action Level

## Slide 31
Health Checkup development – Chemical & Physical Agents
IH Monitoring
(>50%OEL)
Regulatory
(Risk priority in QEA)
Carcinogen Group 1 (IARC)
All Relevant
Agents
Health Check up program
EIA Monitoring Plan

## Slide 32
DOW acceptable OEL
OEL Decision logic

## Slide 33
IHG
TLV ®
WEEL
REG
Harmony
I Need an OEL!
Which OEL should I use?

## Slide 34: Occupational Exposure Limits (OELs) in DOW Chemical
Permissible Exposure Limits (PELs)
  Set by OSHA
  Adopted from 1968 TLVs
  Very hard to change (must prove economic and technical feasibility)
Threshold Limit Values (TLVs)
  Set by ACGIH
  Based on current hazard data
  Changed routinely
Industrial Hygiene Guidelines (IHGs) (Company)
  Set internally by the Dow Chemical Company
  Based on current hazard data
Regulatory Limit (Government)

## Slide 35
Completing the OEL Puzzle:
TLV ®
WEEL
REG
VRG
ACGIH
Government
AIHA
Industry
?

## Slide 36
Industrial Hygiene Guidelines (IHG)
The Dow Chemical Company
IHG

## Slide 37: OEL Puzzle: Dow’s Acceptable OELs
IHG
TLV ®
WEEL
Regs
VRG
ACGIH
Jurisdictions
AIHA
Industry

## Slide 38
Is there any “Logic” ?
Do I use the LOWEST OEL?
5 ppm
3 ppm
1 ppm
10 ppm
100 ppm

## Slide 39
OEL
Decision
Logic

## Slide 40: Dow’s “OEL Decision Logic”
IHG
REG
Use the more
STRINGENT

## Slide 41: Dow’s “OEL Decision Logic”
IHG
TLV ®
WEEL
REG
& / or
& / or
Use the
“most stringent”
OEL
Notes: If no IHG exists, but either a jurisdictional regulation, and /or
  a TLV, and/ or
  a WEEL exists,
  --> use the MOST STRINGENT OEL
If no regulation exists for the jurisdiction, choose the lower of the TLV or WEEL

## Slide 42
Dow’s “OEL Decision Logic”
REG
TLV ®
WEEL
or
& / or
IHG
Use
IHG
Notes: When there is NO Regulatory OEL….. but there is an IHG, TLV, and / or WEEL….. use the IHG
Any time an IHG exists within Dow….. it is used in preference to other external “guidelines”…….. and is compared to any jurisdictional “regulatory OEL” ……. and the more stringent of the 2 is used

## Slide 43
IHG
TLV ®
WEEL
REG
VRG
???

## Slide 44
Vendor Recommend Guidelines (VRGs)
are NOT
used in Dow!!!!

## Slide 45
VRG
Dow’s “OEL Decision Logic”
Issues from Vendor Recommended Guidelines when NO other OEL exists:
  Don’t know rationale for development
  Will review all literature & information available
  Will set Dow IHG
IHG


## Slide 46
Thank you…….